## Slide 1: 3D PRINTING TECHNOLOGY The Security of Mechanical Keys
AN OVERVIEW OF EMERGING TECHNOLOGY AND HOW IT CAN THREATEN TRADITIONAL KEY CONTROL AND SECURITY

## Slide 2: 3D PRINTING TECHNOLOGY: OVERVIEW OF CRITICAL ISSUES
WHO: VIRTUALLY ANYONE CAN OBTAIN A KEY IF THEY HAVE ACCESS TO THE TARGET KEY
WHAT: ANY CONVENTIONAL KEY AND MANY HIGH SECURITY KEYS AND KEYWAYS
WHERE: NO GEOGRAPHIC LIMITATIONS, ESPECIALLY WITH 3D PRINT SHOP ACCESS ON LINE
WHY: TO OBTAIN AN UNAUTHORIZED DUPLICATE KEY OR BLANK TO OPEN A LOCK, OR TO EXTRAPOLATE THE TOP LEVEL MASTER KEY, OR TO DEFEAT THE SECURITY OF A FACILITY

## Slide 3: COMPROMISE OF KEYS MEANS COMPROMISE OF SECURITY
HOW: PHOTOGRAPHY, VISUAL DECODING AND MEASUREMENT, MOLDS, IMPRESSIONS, FAX, EASY ENTRIE FOR KEYWAY REPLICATION, INTERNET PUBLICATION OF SPECIFICATIONS, MANY OTHER TECHNIQUES.
ACCESS TO A TARGRT KEY CAN OFTEN BE EASILY OBTAINED
  BORROWED KEY OR PHYSICAL ACCESS OR POSESSION
  USER IN POSSESSION OF A KEY, EVEN BRIEFLY
  PHOTOGRAPH OF A KEY CARRIED BY ANOTHER PERSON
  PHOTOGRAPH OF A KEYWAY TO MAKE BLANKS + VISUAL DECODING
WHY: TO OBTAIN AN UNAUTHORIZED DUPLICATE KEY OR BLANK TO OPEN A LOCK, OR TO EXTRAPOLATE THE TOP LEVEL MASTER KEY, OR TO DEFEAT THE SECURITY OF A FACILITY

## Slide 4: LOCKS ARE OFTEN THE FIRST AND LAST PHYSICAL BARRIER
CLASSIFICATION OF LOCKS
  Conventional mechanical locks
  High security mechanical locks
  Electro-Mechanical locks
  Electronic cylinders
  Electronic access control systems
  RFID, NFC, Bluetooth Access

## Slide 5: MANY WAYS TO OPEN LOCKS
Picking
Impressioning
Decoding
Bumping
Key simulation, replication, duplication
Master key through extrapolation
Key jiggling and manipulation
Key interchange and unintended master keys

## Slide 6: STANDARDS: LOCKS AND KEYS
UNITED STATES
  Underwriters Laboratories UL 437
  BHMA High Security 156.30
EUROPEAN COMMITTEE FOR STANDARDIZATION
  CEN 1300 High security locks
  CEN 1303 Cylinders for locks

## Slide 7: STANDARDS: WHAT THEY DEFINE
SECURITY LEVELS for MECHANICAL CYLINDERS
  Conventional: Low to Medium security
  High Security: Highest security available
STANDARDS AND SECURITY: HOW DIFFICULT IT IS TO OPEN LOCKS: 3T-2R RULE
  Time
  Tools
  Training
    Reliability of attack
    Repeatability of attack

## Slide 8: CONVENTIONAL CYLINDERS
ATTRIBUTES
No patent protection
No real key control: blank keys are available
Reduced quality of materials
No control over manufacture of blanks
Usually easy to pick, bump, decode, or impression unless enhanced security features
Minimal forced entry protection
Minimal resistance to all forms of attack

## Slide 9: HIGH SECURITY LOCKS
THREE PRIMARY CRITERIA
FORCED ENTRY
  Generally five minutes resistance to attack
  High drill resistance
COVERT ENTRY
  Ten to fifteen minutes resistance to attacks
KEY CONTROL
  Patent protected keys and mechanisms
  Protection from duplication
  Control of blanks and keys
  Restricted keyways

## Slide 10: USE OF CONVENTIONAL LOCKS
MANY FACILITIES DO NOT USE HIGH SECURITY LOCKS
PREDICTABLE RESULTS
  Easy to compromise by forced and covert methods
  Easy to copy keys
  Easy to compromise master key systems
  Easy to bump open
  Often, only the appearance of security

## Slide 11: WHY USE HIGH SECURITY LOCKS Patent Protection
PATENT PROTECTION
  Protected designs of internal mechanism and keys
  Illegal to duplicate, replicate, or manufacture protected keys
  Keys are not readily available without authority
  Keys contain interactive or special elements or designs to make copying and simulation difficult
  More difficult to bump open

## Slide 12: WHY USE HIGH SECURITY LOCKS Resistance to Covert Attacks
COVERT ENTRY
  Secondary locking systems, such as sidebars, rotating pins, sliders, magnetics, telescoping pins
  Multiple sets of active locking components
  Proprietary bitting and side-bit milling
  Complex shapes
  Interactive elements between lock and key

## Slide 13: WHY USE HIGH SECURITY LOCKS Forced Entry Resistance
FORCED ENTRY
  More difficult to open by force:
  Protection against grinding, drilling, sawing, pulling, prying, torque, wrenching
  Special anti-drill protection
  More secure materials
  Higher tolerances

## Slide 14: KEYS FOR MECHANICAL LOCKS: What are they?
A SMALL SOLID OBJECT TO MATE WITH INTERNAL ACTIVE ELEMENTS IN THE LOCK

## Slide 15: KEYS FOR MECHANICAL LOCKS
TRADITIONAL KEYS CAN BE MADE OF MANY MATERIALS
  Metal: brass, nickel silver, steel, aluminum
NON-TRADITIONAL WAYS TO MAKE KEYS
  Plastic
  Epoxy
  Low temperature metals
  Casting

## Slide 16: KEYS: THE COMMON ELEMENT
KEYS ARE THE CRITICAL AND COMMON ELEMENT FOR CONVENTIONAL AND HIGH SECURITY LOCKS
3D PRINTER and SCANNER TECHNOLOGY
  Will force a change in the design of high security keys
  Will require the standards to be upgraded
  Traditional conceptions of key control will change
  New Patent Protection will develop
  Will require a re-evaluation of facility security

## Slide 17: KEYS Conventional vs. High Security
WIDESPREAD AVAILABILITY vs. KEY CONTROL
KEYWAYS: COMMERCIAL vs. RESTRICTED
SECTIONAL KEYWAYS
BITTING: Traditional, dimple, angled, unique shapes, multiple rows
MOVABLE OR INTERACTIVE ELEMENTS: Examples: Mul-t-Lock, Keso, Vachette, Tesa
MAGNETICS: Evva
ELECTRONIC ELEMENTS
MULTIPLE SECURITY LAYERS: Secondary bitting examples: Medeco, Primus, Assa Twin

## Slide 18: THE EASIEST WAY TO OPEN A LOCK: With a Key

## Slide 19: TRADITIONAL METHODS TO PRODUCE MECHANICAL KEYS
TWO PRIMARY ISSUES:
Obtaining or producing the blanks
Creating the bitting and knowing the values
  Key machines: manual copying or code cutting
  Impressioning the lock
  Impression of the key (Great Train Robbery)
  Molds, Silicone, Epoxy
  Photography and milling machine
  Decoding by micrometer or gauge and hand-filing or code cutting
  Visual decoding for bitting levels
  Disassembly of lock and determining bitting values
  Decoding tools
  Variable key simulation systems
  Easy Entrie milling machine

## Slide 20: EASY ENTRIE MILLING MACHINE

## Slide 21: EASY ENTRIE PROBE KEY BLANK MEASUREMENT

## Slide 22: MILLED BLANKS

## Slide 23: MILLING OF BLANKS WITH EAS ENTRIE

## Slide 24: SECURITY AGAINST DUPLICATION, SIMULATION, OR REPLICATION
METHODS TO ENHANCE KEY CONTROL
Unique keyways
Undercuts
Complex bitting
Side-bit milling, angled cuts
Unique or difficult-to-decode bitting patterns
Multiple or complex angles or bores in bitting
Interactive elements
Magnetics
Electronic elements
THE REAL WORLD
“Do Not Duplicate”
Patent protection

## Slide 25: CONVENTIONAL KEYS: KEY SECURITY
EASY AVAILABILITY OF BLANIKS
DEPTH AND SPACE INFORMATION AVAILABLE
NO SPECIAL CUTTER REQUIRED
CAN BE PHOTOGRAPHED AND DECODED
NO RESTRICTIONS ON ACCESS TO KEYS
EASY TO MAKE BUMP KEYS WHICH WILL OPEN MOST PIN TUMBLER LOCKS

## Slide 26: CONVENTIONAL KEYS: MINIMAL SECURITY

## Slide 27: HIGH SECURITY LOCKS: PHYSICAL KEY SECURITY
PATENT PROTECTED
RESTRICTED KEYWAYS
PHYSICAL PROTECTIVE MEASURES
COMPLIANCE WITH UL, BHMA STANDARDS
MORE DIFFICULT TO DUPLICATE, SIMULATE, OR REPLICATE

## Slide 28: DIFFERENT SECURITY MEASURES Special bitting designs

## Slide 29: DIFFERENT SECURITY MEASURES Interactive elements

## Slide 30: DIFFERENT SECURITY MEASURES Interactive elements

## Slide 31: NEW TECHNOLOGY: NEXT GENERATION TO REPRODUCE KEYS
Scanners
High-resolution photographs
3D printers
Inexpensive computer-controlled milling machines
Materials other than metals
Remote file servers
On-line print shops “Kinko’s for keys”

## Slide 32: 3D PRINTER TECHNOLOGY: SIX CRITICAL QUESTIONS
WHAT IS IT?
HOW DOES IT WORK?
HOW DIFFICULT TO PRODUCE KEYS?
ACCESS TO TECHNOLOGY?
AVAILABILITY AND COST?
IS IT A THREAT TO SECURITY?

## Slide 33: 3D PRINTER REVOLUTION
Availability everywhere, even at Microsoft stores
Upload files to print shop
Download files from server
Parts on demand
Price from $1000-$650,000
3D is a software-bases system
STL files, CAD output
Key not difficult to develop and generate
Images from scanners and high res photographs

## Slide 34: 3D PRINTED PARTS

## Slide 35: 3D PRINTED LOCK

## Slide 36: 3D PRINTED LOCK

## Slide 37: ISSUES RELATING TO SECURITY
Legal
Technical
Intellectual Property
Security
Standards regarding Key Control
Access to blanks and Protection of master key systems
Production of bump keys
3D Print commercial print houses, enforcement of Intellectual Property Rights

## Slide 38: OUR 3D RESEARCH PROJECT: It started at M I T and DefCon 21

## Slide 39: SCHLAGE PRIMUS ORIGINAL KEY

## Slide 40: THE PROBLEM: TECHNOLOGY HAS CAUGHT UP WITH A PIECE OF METAL CALLED A KEY
3D PRINTER TECHNOLOGY
Can duplicate restricted keys
Can create blanks for high security systems
Can replicate or simulate some interactive elements
Can create some forms of springs
Can scan keys and feed directly to printers
Can upload and download files of key profiles and bitting from online servers
Can violate patent protection with little remedy

## Slide 41: METAL KEYS vs. 3D TECHNOLOGY MORE PROBLEMS
CONVENTIONAL AND SOME HIGH SECURITY KEYS
Can be easily decoded
Keyways can be replicated from photographs
Keys can be easily copied
Traditional key control can be circumvented
Employees can obtain copies of keys
Restricted keyways circumvented
Physical presence not required to obtain a key
Key profiles may be available for download

## Slide 42: WHAT CAN’T 3D DO TODAY?
REPRODUCE MAGNETIC ELEMENTS
REPRODUCE ELECTRONIC CREDENTIALS
PRINT ORGANIC MATERIALS
BUT NOT SO FAST!

## Slide 43: MAGNETIC-BASED KEY ELEMENTS EVVA Magnetic Code System

## Slide 44: KEY WITH BITTING AND CREDENTIALS For Electro-mechanical Cylinders

## Slide 45: ELECTRONIC CREDENTIALS: For E-Cylinders

## Slide 46: 3D CANNOT DO TODAY: But probably tomorrow
  Can embed foreign elements like magnets
  Can mix materials like plastic and metal
  Can create or simulate spring-biased elements
  Will be able to print circuitry

## Slide 47: 3D BASICS
THREE-DIMENSIONAL SOLID OBJECTS FROM ANY SHAPE FROM A DIGITAL MODEL
ADDITIVE PROCESS REATHER THAN SUBTRACTIVE LIKE MACHINING
DEVELOPED IN 1980s
BUILDS LAYERS WITH DIFFERENT MATERIALS
USES PLASTICS, NYLON, ABS, METALS
CAN CREATE MOLDS FOR CASTING
USES LASERS AND HIGH TEMPERATURE
COMPARE TO INK JET PRINTERS

## Slide 48: 3D RESOLUTION
3D PRINTABLE FILES (STL FORMAT)
PRINTER RESOLUTION X-Y IN dpi OR MICROMETERS
TYPICAL RESOLUTION: 250 dpi = 100 µm .004”
HIGH RESOLUTION 1600 dpi = 16 µm = .0006”
PROCESSES: THE WAY LAYERS ARE DEPOSITED AND MATERIALS

## Slide 49: 3D PROCESSES
SLM = SELECTIVE LASER MELTING Melt or soften material to produce layers
DMLS = DIRECT METAL LASER SINTERING
SLS = SELECTIVE LASER SINTERING
FDM = FUSED DEPOSITION MODELING
SLA = STEREO LITHOGRAPHY
LOM = LAMINATED OBJECT MANUFACTURING

## Slide 50: MAKERBOT POPULAR FDM PRINTER

## Slide 51: MAKERBOT PRINT HEAD

## Slide 52: PROFESSIONAL PRINT HOUSES: High Resolution Capabilities

## Slide 53: SECURITY THREATS FROM 3D PRINTING TECHNOLOGY
PRODUCTION OF BLANK KEYS
To duplicate keys without authorization
Create blanks from photographs of keyways
Download restricted blanks with bitting after decoding the target key
Create bump keys for virtually any keyway
Compromise master key systems

## Slide 54: PROCESSES AND MATERIALS
FDM FUSED DEPOSITION MODELING
2 = nozzle ejecting molten plastic
3 = deposited material

## Slide 55: ORIGINAL PRIMUS TO 3D CREATED KEY

## Slide 56: 3D THREAT: BLANKS TO CREATE BUMP KEYS

## Slide 57: BUMP KEY

## Slide 58: CREATION OF BLANKS
PHOTOGRAPH OF KEYWAY
PROCESS THROUGH SOFTWARE LIKE ADOBE
TRANSLATE TO 3D PRINT FILE OR EASY ENTRIE

## Slide 59: 3D PRINTED BLANK: PHOTOGRAPH TO STL FILE

## Slide 60: JOS WEYERS: SPORT LOCKPICKING

## Slide 61: 3D CREATED BUMP KEYS

## Slide 62: THE THREAT FROM BUMP KEYS

## Slide 63: 3D CREATED BUMP KEY

## Slide 64: JOS WEYERS: BLANKS FROM KEYWAYS

## Slide 65: TOP LEVEL MASTER KEY DECODING KEY BLANK ARE CRITICAL

## Slide 66: MASTER KEY SYSTEM EXTRAPOLATION

## Slide 67: SUMMARY
THE NEW TECHNOLOGY IS A GREATER THREAT THAN LOCK BUMPING
WILL REQUIRE NO SKILL TO DUPLICATE A KEY: JUST MONEY
PRESENT KEY CONTROL WITH REGARD TO BLANK ACCESS AND DUPLICATION WILL BE CIRCUMVENTED
BHMA HIGH SECURITY LOCK STANDARDS WILL BE INEFFECTIVE AND NEED TO BE MODIFIED FOR HIGH SECURITY SYSTEMS
MANUFACTURERS WILL RESPOND WITH 3D-SECURE BLANKS AND SYSTEMS

## Slide 68: SUMMARY
CAN AFFECT VIRTUALLY ALL MECHANICAL KEYS UNLESS THEY CONTAIN CERTAIN INTERACTIVE ELEMENTS
ALL CONVENTIONAL KEYS WILL BE SUBJECT TO ATTACK
MANY HIGH SECURITY KEYS WILL BE ABLE TO BE COPIED
INTERNAL THREAT TO SECURITY BY KEYMAIL, OR PHOTOGRAPH OF KEYS

## Slide 69: SECURITY VULNERABILITIES NOW AND IN THE FUTURE
3D IS NOT MAINSTREAM YET
CONSUMER 3D PRINTERS NOT HIGH RESOLUTION, ONLY FOR CONVENTIONAL KEYS
SOME SKILL IS NEEDED TO PRODUCE KEYS
ON-LINE PRINT HOUSES ARE THE THREAT
REMOTE FILE SERVERS AND PROFILES
SCANNERS + HIGH RES PRINTER THREAT
MANY WAYS TO PRODUCE KEYS, 3D IS ONLY ONE OF THEM
THE SKY IS NOT FALLING, YET
HIGH SECURITY FACILITIES SHOULD PLAN FOR FUTURE SYSTEMS

## Slide 70: REGULATION AND LEGISLATION
Trafficking in patented designs and restricted keyways including:
  Public safety systems
  DoD and USPS
  Fire Department building access
  Keys for critical infrastructure
Equivalent to Digital Millennium Copyright Act

## Slide 71: JEFF HANSON STRATASYS-REDEYE

## Slide 72: SECURITY LABS INVESTIGATIVE LAW OFFICES
© 2014 Marc Weber Tobias
Contact: mwtobias@security.org
1.605.334.1155