## Slide 1: MEDECO “VIRTUALLY RESISTANT” SECURITY
A Case Study in Real World
Security Vulnerabilities and Liability

## Slide 2: LOCKS AND LIABILITY: WHY IMPORTANT
PROTECTION OF ASSETS, INFORMATION, PEOPLE
PREVENT LOSSES
UNAUTHORIZED ACCESS
STATUTORY REQUIREMENTS
STANDARDS: MINIMAL PROTECTION
BYPASS OF LOCKS
ELECTRONIC ACCESS CONTROL

## Slide 3: MEDECO: One of the Most Secure Locks in America?
FORTY YEARS: THE LEADER
FIRST LINE OF PROTECTION
CRITICAL INFRASTRUCTURE
LEGAL REQUIREMENTS
HIGHEST SECURITY RATINGS
  UL 437 and BHMA/ANSI 156.30

## Slide 4: MEDECO CASE STUDY: WHY IMPORTANT
CONCEPT OF SECURITY
  Medeco locks are good, but not for everybody
STANDARDS DO NOT PROTECT YOU
CORPORATE ARROGANCE
  Medeco cannot open their own locks
  “Nobody else understands their locks”
CAMPAIGN OF DISINFORMATION
  Misrepresentations, obfuscation, and misstatements

## Slide 5: MEDECO: LESSONS LEARNED
PATENTS DO NOT MEAN ANYTHING
STANDARDS: LIMITED VALUE
SOME MANUFACTURERS WILL NOT TELL THE TRUTH OR DO NOT KNOW
KEY CONTROL: THE MYTH
SECURITY OF MECHANICAL LOCKS
ELECTRONIC ACCESS CONTROL SECURITY ISSUES

## Slide 6: LOCK BUMPING: WHERE IT ALL STARTED
AUGUST 2006: JENNALYNN
  Bumps a Kwikset pin tumbler lock
AUGUST 2007: JENNALYNN
  Bumps a Medeco Biaxial lock
JUNE, 2008: OPEN IN THIRTY SECONDS
AUGUST, 2008: JENNALYNN
  Bumps a Medeco with ARX pins

## Slide 7: LOCK BUMPING THEORY

## Slide 8: JENNALYNN, AGE 11: OPENS KWIKSET

## Slide 9: LOCK BUMPING: 2006 A SERIOUS THREAT
INTRODUCED LOCK BUMPING
  JennaLynn opens a Kwikset
KNOWN TECHNIQUE: 1925
  Refined in 2004 in Europe
ALOA: NOT A PROBLEM
MEDECO: BUMP-PROOF LOCKS
POSTAL INSPECTION SERVICE
CONVENTIONAL LOCKS AFFECTED

## Slide 10: WHY BUMPING IMPORTANT
EXPOSED VULNERABILITY TO 95% OF PIN TUMBLER LOCKS
PUBLIC AWARENESS
LEGAL NOTICE AND LIABILITY
HIGH SECRITY LOCKS
  Manufacturers said locks were secure
  Our locks are bump-proof
  Assa Abloy Companies: “Smoke and mirrors”

## Slide 11: BUMPING AND SECURITY
NEED TO UNDERSTAND PROBLEM
PROPERLY ASSESS SECURITY
RESULTED IN BYPASS OF HIGH SECURITY LOCKS
  MEDECO, MUL-T-LOCK, ASSA, OTHERS
LEGAL LIABILITIES AND STATUTORY MANDATES FOR SECURITY

## Slide 12: WHAT IS HIGH SECURITY: QUESTIONS TO ASK
DO I HAVE HIGH SECURITY LOCKS
DO I NEED HIGH SECURITY LOCKS
CAN HIGH SECURITY LOCKS BE COMPROMISED
WHAT CONSTITUTES A THREAT AND HOW DO LOCKS PROTECT MY FACILITY
WILL ELECTRONIC ACCESS CONTROL BE SUFFICIENT

## Slide 13: HIGH SECURITY LOCKS: A REVIEW
SPECIFY FOR FACILITY PROTECTION
  COVERT ENTRY
  FORCED ENTRY
  KEY CONTROL
MINIMUM SECURITY CRITERIA
  MINIMUM ATTACK TIMES
  RESISTANCE TO CERTAIN FORMS OF ENTRY
  UL 437 and BHMA/ANSI 156.30

## Slide 14: COVERT ENTRY PROTECTION: The Theory
MINIMUM SECURITY CRITERIA IN UL 437 and BHMA/ANSI 156.30
PROTECT AGAINST CERTAIN FORMS OF COVERT ENTRY
ASSURE MINIMUM RESISTANCE TIMES TO OPEN

## Slide 15: COVERT ENTRY OF MEDECO LOCKS: RESULT
BUMPING
  Modified change key
  Simulated key
PICKING
  With change key
  With code setting keys
EXTRAPOLATE TMK
DECODE BILEVEL SYSTEM TO COMPROMISE m3 SYSTEM

## Slide 16: MEDECO INSECURITY: Real World Threats - Covert
FOUR KEYS TO PICK AND BUMP PRE-12/07 LOCKS
SIXTEEN OR LESS KEYS FOR 2008 LOCKS
PICKING IN AS LITTLE AS 27 SECONDS
  Using any change key on same sidebar code
  With code setting keys
  Angle setting keys
  ARX pins

## Slide 17: MEDECO INSECURITY: Real World Threats - Covert
BUMPING
  With correct blank and sidebar code
  With simulated blank
  With or without ARX pins

## Slide 18: BUMPING MEDECO LOCKS

## Slide 19: FORCED ENTRY PROTECTION: Theory
LOCKS ARE SECURE AGAINST FORCED METHODS OF ATTACK
MINIMUM TIMES SPECIFIED IN UL 437 and BHMA/ANSI 156.30
ATTACK RESISTANCE: 5 MINUTES

## Slide 20: MEDECO INSECURITY: Real World Threats – Forced
DEADBOLT Pre-12/2007
  Thirty seconds
  Complete circumvention of security
  Simple tools, easy to accomplish
DEADBOLT 2008
  Reverse picking attack
MORTISE, RIM, ICORE
  Hybrid attack, compromise of key control

## Slide 21: MEDECO INSECURITY: Real World Threats - Keys
VIOLATION OF KEY CONTROL and KEY SECURITY
  Compromise of entire facility
  Improper generation of keys
  Compromise of Top Level Master Key

## Slide 22: MEDECO INSECURITY: The Threat from Within
COMPROMISE OF KEY CONTROL + HYBRID ATTACK
  Mortise, Rim, Interchangeable cores
MEDECO KEY CONTROL v. CONVENTIONAL KEYS
  Conventional keys = 1 layer of security
  Medeco keys = 3 layers of security
  Electronic Access Control issues: two levels of security

## Slide 23: MEDECO INSECURITY: The Threat from Within
OBTAIN KEY DATA TO OPEN LOCKS BY HYBRID ATTACK
KEY CONTROL IS CIRCUMVENTED
BRIEF ACCESS TO A KEY FOR A TARGET LOCK
  Compromise of the lock or system
  By insiders
  By criminals outside of an organization

## Slide 24: MEDECO KEY CONTROL: Appearance v. Reality
WHAT IS IT SUPPOSED TO MEAN?
ARE THE STANDARDS SUFFICIENT?
REAL WORLD VULNERABILITIES
IS ELECTRONIC ACCESS CONTROL ANY MORE SECURE?

## Slide 25: KEY CONTROL: The Theory
PROTECTION OF BLANKS OR CUT KEYS FROM ACQUISITION OR USE:
  Unauthorized duplication
  Unauthorized replication
  Unauthorized simulation
    restricted keyways
    proprietary keyways
    sectional keyways

## Slide 26: KEYS and KEY CONTROL
KEYS ARE THE EASIEST WAY TO OPEN LOCKS
  Change key or master key
  Duplicate correct bitting
  Bump keys
  Rights amplification: modify keys
PROTECTION OF KEYS
  Side bit milling: Primus and Assa
  Interactive elements: Mul-T-Lock
  Magnets: EVVA MCS

## Slide 27: PROTECTION OF KEYS

## Slide 28: PROTECTION OF KEYS

## Slide 29: MEDECO KEYMARK: ABSOLUTE KEY CONTROL!

## Slide 30: MEDECO KEYMARK X4

## Slide 31: KEYMARK TAKES PLASTIC

## Slide 32: SECURITY THREAT: Failure of Key Control: Duplicate
IMPROPER ACQUISITION OR USE OF KEYS BY EMPLOYEES OR CRIMINALS
Unauthorized access to facilities or areas
Bump keys
Use for rights amplification
Compromise master key systems

## Slide 33: KWIKSET: CONVENTIONAL LOCKS AND KEYS

## Slide 34: SECURITY THREAT: Failure of Key Control: Replicate
HIGH SECURITY LOCKS AND KEYS
  Designed to prevent replication
REPLICATION TECHNIQUES
EASY ENTRIE MILLING MACHINE
SILINCONE CASTING
PLASTIC AND EPOXY

## Slide 35: SECURITY THREAT: Failure of Key Control: Simulate
M3 KEYWAY
  Wider than Biaxial
  No paracentric keyway
COMPONENTS OF MEDECO KEYS
  Ward pattern and paracentric keyway
  Bitting
  M3 Slider
SECURITY THREAT
  Bypass wards in paracentric keyway
  Create new blanks

## Slide 36: RESULT: Failure of Key Control
Restricted and proprietary keyways
M3 Slider: bypass with paper clip
Sabotage potential
Make keys to open your locks
Duplicate from codes or pictures
TMK extrapolation
Set the sidebar code

## Slide 37: DUPLICATING MEDECO

## Slide 38: KEYS AND FORCED ENTRY

## Slide 39: COMPROMISE THE SYSTEM: Obtaining the Critical Data
TECHNIQUES TO OBTAIN KEY DATA
Impressioning methods
Decoding: visual and Key Gauges
Photograph
Scan keys
Copy machine

## Slide 40: KEY CONTROL: Why Most Keys are Vulnerable
CONVENTIONAL LOCKS: Single Layer
  KEYWAY = KEY CONTROL
LEGAL PROTECTION DOES NOT PREVENT REAL WORLD ATTACKS
  KEYS = BITTING HEIGHT + KEYWAY
  Bypass the keyway
  Raise pins to shear line

## Slide 41: MEDECO KEY CONTROL: Virtually Impossible to Copy
“If there is no key control, then it does not matter what security enhancements are in the lock”

## Slide 42: MEDECO KEY CONTROL: The Problem
CIRCUMVENTING SECURITY LAYERS
  KEYWAYS CAN BE BYPASSED
  BLANKS CAN BE SIMULATED
  SIDEBAR CODES ARE SIMULATED
  SLIDER CAN BE BYPASSED
NO REAL LEGAL PROTECTION EXCEPT FOR M3 STEP

## Slide 43: MORTISE, RIM, IC: A Special Form of Attack
HYBRID ATTACK
Will damage the lock
Entry in ten seconds
Millions of Locks affected

## Slide 44: “KEYMAIL”: The New Security Threat from Within
NEW AND DANGEROUS THREAT
THE NEW MULTI-FUNCTION COPIER
It scans, copies, prints, and allows the production of MEDECO keys

## Slide 45: KEYMAIL: How It Works for Mortise, IC, and Rim Cylinders
ACCESS TO THE TARGET KEY
CAPTURE AN IMAGE
PRINT THE IMAGE
PRODUCE A KEY
OPEN THE LOCK

## Slide 46: PLASTIC KEYS: PROCEDURE
OBTAIN IMAGE OF THE KEY
  Scan, copy, or photograph a Medeco key
  Email and print the image remotely
  Print 1:1 image on paper or plastic Shrinky Dink
  Trace onto plastic or cut out the key bitting
INSERT KEY INTO PLUG
  Neutralize three layers of security
  Open Mortise, Rim, IC cylinders

## Slide 47: ACCESS TO TARGET KEY
BORROW BRIEFLY
AUTHORIZED POSSESSION
USE
COLLUSION WITH EMPLOYEE WHO HAS ACCESS TO A KEY

## Slide 48: CAPTURE AN IMAGE
COPIER
TRACE THE KEY
CELL PHONE CAMERA
SCANNER

## Slide 49: OBTAIN DATA - COPIER

## Slide 50: OBTAIN DATA
SCANNER

## Slide 51: OBTAIN DATA
CELL PHONE

## Slide 52: BLACKBERRY CURVE
CAPTURED IMAGE

## Slide 53: RESULTING IMAGE
REPRODUCE THE IMAGE
  On Paper
  On plastic sheet
  On Adhesive Labels
  On Shrinky dinks® plastic
  On a piece of copper wire
  On a simulated metal key

## Slide 54: PRINT IMAGE ON PLASTIC OR PAPER

## Slide 55: SET THE SHEAR LINE
PLASTIC KEY SETS SHEAR LINE

## Slide 56: SET THE SHEAR LINE

## Slide 57: SET THE SHEAR LINE

## Slide 58: CUT A FACSIMILE OF KEY
KEY REQUIREMENTS
  Vertical bitting only
  No sidebar data
  No slider data

## Slide 59: SET THE SHEAR LINE: OPEN THE LOCK

## Slide 60: NEUTRALIZE SHEAR LINE

## Slide 61: HIGH SECURITY LOCK MANUFACTURERS
LEGAL RESPONSIBILITY
ETHICAL RESPONSIBILITY
  NOTIFY OF VULNERABILITIES
  PROPER PRODUCT DESIGNS
  FIX PROBLEMS

## Slide 62: LOCKS, LIES, AND VIDEOTAPE: MEDECO CASE STUDY
LOCK BUMPING: WHERE IT BEGAN
MEDECO CASE STUDY
  Medeco security: “Our locks are bump-proof, virtually bump-proof, and Virtually Resistant”
  We Never claimed our Locks were bump-proof!
  Our deadbolts are secure, no problem!
  We have spent hundreds of hours and cannot replicate any of the Tobias attacks!

## Slide 63: MEDECO BUMPING CLAIM: “We never said it: Others did!”
WHAT IS THE TRUTH?
  August 4, 2006 press release: “Bump-proof”
  2007 - Retroactively changed the language: “Virtually Bump-proof”
  The Medeco Problem: www.archive.org
TV, Advertising, DVD, Medeco website
The Smoking Gun: August 12, 2006

## Slide 64: WE NEVER SAID OUR LOCKS WERE BUMP-PROOF
AUGUST 15, 2006
U.S. Patent and Trademark Office filing by Medeco Security Locks, Inc. lawyer G. Franklin Rothwell, Application 78952460
Word mark: BUMP PROOF
Abandoned: February 9,2007

## Slide 65: BUMP PROOF: USPTO FILING FOR THE WORD MARK

## Slide 66: ABOUT CLAIMS OF PICKING MEDECO LOCKS
NOBODY HAS PROVED THEY CAN PICK OUR LOCKS IN 40 YEARS
  False demonstrations, special locks
  They are lying
  We cannot replicate anything
THE REAL PROBLEM
  They cannot open their own locks
  Failure of imagination

## Slide 67: RESPONSIBLE DISCLOSURE BY LOCK MANUFACTURERS
KNOWLEDGE OF VULNERABILITY
Known or suspected
Make responsible notifications
Let users and dealers assess risks
Duty to tell the truth
Duty to fix the problem

## Slide 68: VULNERABILITIES: Full Disclosure Required
SECURITY BY OBSCURITY
It does not work with Internet
It is the User’s security
They have a right to assess their own risks
Criminals already have information
Disclosure: benefits outweigh risks
Liability for failure to disclose

## Slide 69: LESSONS LEARNED
THE MEDECO CASE
Nothing is impossible
Corporate arrogance does not work
HIGH SECURITY LOCK MAKERS
Engineering, Security, Integrity
Duty to tell the truth

## Slide 70: OPEN IN THIRTY SECONDS
© 2008 Marc Weber Tobias, Matt Fiddler
http://www.security.org
http://in.security.org
mwtobias@security.org
mjfiddler@security.org
tbluzmanis@security.org