## Slide 1: MEDECO CASE STUDY
Cracking One of the Most Secure Locks in America
Lessons learned from embedded design deficiencies, a failure of imagination, and a failure to connect the dots, and a belief in invincibility

## Slide 2: MEDECO LOCKS PROTECT THE ROYAL PALACE IN LONDON

## Slide 3: MEDECO HIGH SECURITY

## Slide 4: MEDECO HIGH SECURITY: What it means
UL, BHMA/ANSI, Vd.S Certified
High level of protection against attack
Picking: 10-15 minute resistance
No bumping
Forced Entry: 5 minutes, minimum
Key control
  Protect restricted and proprietary keyways
  Stop duplication, replication, simulation of keys

## Slide 5: STORY OF LOCKS, LIES, and HIGH INSECURITY
Dominant high security lock maker
40 year history of security
Many expert attempts to crack with limited success, complicated tools
Misstatements and disinformation
18 month research project results:
Total compromise of security

## Slide 6: HIGH SECURITY LOCKS: Why Important?
Protect Critical Infrastructure, high value targets
Stringent security requirements
High security Standards
Threat level is higher
Protect against Forced, Covert entry
Protect keys from compromise

## Slide 7: MEDECO HISTORY
Dominant high security lock maker in U.S.
Owns 70+ Percent of U.S. high security market for commercial and government
Major government contracts
In UK, France, Europe, South America
Relied upon for highest security everywhere
Considered almost invincible by experts

## Slide 8: WHY THE MEDECO CASE STUDY IS IMPORTANT
Insight into design of high security locks
Patents are no assurance of security
Appearance of security v. Real World
Undue reliance on Standards
Manufacturer knowledge and Representations
Methodology of attack
More secure lock designs

## Slide 9: CONVENTIONAL v. HIGH SECURITY LOCKS
CONVENTIONAL CYLINDERS
  Easy to pick and bump open
  No key control
  Limited forced entry resistance
HIGH SECURITY CYLINDERS
  UL and BHMA/ANSI Standards
  Higher quality and tolerances
  Resistance to Forced and Covert Entry
  Key control

## Slide 10: ATTACK METHODOLOGY FOR HIGH SECURITY LOCKS
Assume and believe nothing
Ignore the experts
Think “out of the box”
Consider prior methods of attack
Always believe there is a vulnerability
WORK THE PROBLEM
  Consider all aspects and design parameters
  Do not exclude any solution

## Slide 11: HIGH SECURITY LOCKS: Critical Design Issues
Multiple security layers
More than one point of failure
Each security layer is independent
Security layers operate in parallel
Difficult to derive intelligence about a layer

## Slide 12: HIGH SECURITY: Three Critical Design Factors
Resistance against forced entry
Resistance against covert and surreptitious entry
Key control and “key security”
Vulnerabilities for each requirement

## Slide 13: QUESTIONS: BYPASS AND REVERSE ENGINEERING
Weakest link in lock to bypass (Medeco)
What locks the lock?
What locking elements lock and in what order. Is there a primary element to bypass?
Result if one layer fails: Can others be compromised?
What intelligence needed to open the lock?
Can Intelligence be simulated?

## Slide 14: SYSTEM BYPASS: More Questions
How strong is the sidebar(s) against forced attack
Is the sidebar the only locking system?
What if defeat one of two sidebars or security layers?
Bitting design: spring biased?
Ability to manipulate each pin or slider to set its code?

## Slide 15: EXPLOIT DESIGN FEATURES AND SYSTEM PARAMETERS
Codes: design, progression
Key bitting design
Tolerances
Keying rules
  Medeco master and non-master key systems
Interaction of critical components and locking systems
Keyway and plug design

## Slide 16: ATTACKS: Two Primary Rules
“The Key never unlocks the lock”
  Mechanical bypass
Alfred C. Hobbs: “If you can feel one component against the other, you can derive information and open the lock.”

## Slide 17: METHODS OF ATTACK: High Security Locks
Picking and manipulation of components
Impressioning
Bumping
Vibration and shock
Shim wire decoding (Bluzmanis and Falle)
Borescope and Otoscope decoding
Direct or indirect measurement of critical locking components

## Slide 18: ADDITIONAL METHODS OF ATTACK
Split key, use sidebar portion to set code
Simulate sidebar code
Use of key to probe depths and extrapolate
Rights amplification of key

## Slide 19: KEY CONTROL
High security requirement

## Slide 20: KEY CONTROL and “KEY SECURITY”
Duplicate
Replicate
Simulate
“Key control” and “Key Security” may not be synonymous!

## Slide 21: KEY SECURITY: A Concept
Key control = physical control of keys
Prevent manufacture and access to blanks
Control generation of keys by code
Patent protection
Key security = compromise of keys
  Duplication
  Replication
  Simulation

## Slide 22: KEYS: CRITICAL ELEMENTS
Length = number of pins/sliders/disks
Height of blade = depth increments = differs
Thickness of blade = keyway design
Paracentric design
Keyway modification to accommodate other security elements
  Finger pins
  Sliders

## Slide 23: KEY CONTROL: Critical issues
Simulation of code or key components
Security of locks = key control and key security
  All bypass techniques simulate actions of key
  Easiest way to open a lock is with the key

## Slide 24: KEY CONTROL and “KEY SECURITY” ISSUES
Most keys are passive: align = open
Simulate components of key
Replicate critical components
Duplicate critical components
Require interactive element for security
  MUL-T-LOCK element
  MCS magnets

## Slide 25: KEY CONTROL: Design Issues
Bitting design
Bitting and sidebar issues and conflicts and limitations in differs
Ability to decode one or more keys to break system
Consider critical elements of the key: require to insure cannot be replicated
Hybrid attacks using keys
  Medeco mortise cylinder example

## Slide 26: DUPLICATION AND REPLICATION OF KEYS
Key machine
Milling machine: Easy Entrie
Clay and Silicone casting
Key simulation: Medeco
Rights amplification
Alter similar keys

## Slide 27: COVERT and FORCED ENTRY RESISTANCE
High security requirement

## Slide 28: STANDARDS REQUIREMENTS
UL and BHMA/ANSI STANDARDS
TIME is critical factor
  Ten or fifteen minutes
  Depends on security rating
Type of tools that can be used
Must resist picking and manipulation
Standards do not contemplate more sophisticated methods

## Slide 29: CONVENTIONAL PICKING

## Slide 30: TOBIAS DECODER: Medeco decoder: by “Crackpot!”

## Slide 31: SOPHISTICATED DECODERS
John Falle: Wire Shim Decoder

## Slide 32: DECODE PIN ANGLES

## Slide 33: FORCED ENTRY RESISTANCE
High security requirement

## Slide 34: FORCED ENTRY ATTACKS: Deficiencies in standards
Many types of attacks defined
Do not contemplate mechanical bypass
Must examine weakest linkis
Do not cover “hybrid attacks”
  Medeco deadbolt attacks
  Medeco mortise attack

## Slide 35: SIDEBAR: Bypass and Circumvention
Direct Access
  Decoding attacks
  Manipulation
  Simulate the sidebar code (Medeco)
  Use of a key (Primus and Assa
Indirect access
  Medeco borescope and otoscope decode issues

## Slide 36: SIDEBAR ATTACK: Physical Strength
Independent protection
Integrated with pin tumblers or other critical locking components
Compress plug
Defeat of sidebar as one security layer: result and failures
Anti-drill protection

## Slide 37: FORCED ENTRY ATTACKS
Direct compromise of critical components
  Medeco deadbolt 1 and 2 manipulate tailpiece
Hybrid attack: two different modes
  Medeco reverse picking
Defeat of one security layer: result
  Medeco Mortise and rim cylinders, defeat shear line

## Slide 38: MEDECO HIGH SECURITY: Lessons to be learned
What constitutes security
Lessons for design engineers
Appearance v. reality

## Slide 39: MEDECO CASE HISTORY
Exploited vulnerabilities
Reverse engineer sidebar codes
Analyze what constitutes security
Analyze critical tolerances
Analyze key control issues
Analyze design enhancements for new generations of locks: Biaxial and m3 and Bilevel

## Slide 40: MEDECO MISTAKES
Failed to listen
Embedded design problems from beginning
Compounded problems with new designs with two new generations: Biaxial and m3
Failed to “connect the dots”
Failure of imagination
Lack of understanding of bypass techniques

## Slide 41: DESIGN = VULNERABILITIES
Basic design: sidebar legs + gates
  How they work: leg + gate interface
  Tolerance of gates
Biaxial code designation
Biaxial pin design: aft position decoding
M3 slider: geometry
M3 keyway design
Deadbolt design

## Slide 42: MEDECO DESIGN: Exploit design vulnerabilities
EXPLOIT BEST DESIGN FEATURES
Sidebar leg – true gate channel
Code assignment: Biaxial 1985
Gate – sidebar leg tolerance
M3 design 2003
  Widen keyway .007”
  Slider geometry, .040” offset

## Slide 43: MEDECO TIMELINE
1970 Original Lock introduced
1985 Biaxial, Second generation
2003 m3 Third generation
2006 Bumping introduced to America
  Medeco announces “Bump-Proof”
2007 Revised to “Virtually Bump-Proof”
2007 Revised to “Virtually Resistant”
2008 No public statements by Medeco

## Slide 44: MEDECO LOCKS: Why are they Secure?
2 shear lines and sidebar for Biaxial
3 independent security layers: m3
Pins = 3 rotation angles, 6 permutations
Physical pin manipulation difficult
False gates and mushroom pins
ARX special anti-pick pins
High tolerance

## Slide 45: MODERN PIN TUMBLER

## Slide 46: MEDECO BIAXIAL

## Slide 47: MEDECO LOCKS: 3 Independent Security Layers
Layer 1: PIN TUMBLERS to shear line
Layer 2: SIDEBAR: 3 angles x 2 positions
Layer 3: SLIDER – 26 positions
TO OPEN:
  Lift the pins to shear line
  Rotate each pin individually
  Move the slider to correct position

## Slide 48: MEDECO TWISTING PINS: 3 Angles + 2 Positions

## Slide 49: SIDEBAR AS A GENERIC SECURITY CONCEPT
Block rotation of the plug
One or two sidebars
Primary or secondary locking
Only shear line or secondary
Integrated or separate systems
  Assa, Primus , MT5, MCS= split
  Medeco and 3KS = integrated
Direct or indirect relationship and access by key bitting

## Slide 50: SECURITY CONCEPTS: Sidebar IS Medeco Security
GM locks, 1935, Medeco re-invented
Heart of Medeco security and patents
Independent and parallel security layer
Integrated pin: lift and rotate to align
Sidebar blocks plug rotation
Pins block manipulation of pins for rotation to set angles

## Slide 51: PLUG AND SIDEBAR: All pins aligned

## Slide 52: SIDEBAR RETRACTED

## Slide 53: PLUG AND SIDEBAR: Locked

## Slide 54: MEDECO CODEBOOK: At the heart of security
All locksmiths worldwide must use
All non-master keyed systems
New codes developed for Biaxial in 1983
Chinese firewall: MK and Non-MK
Codebook defines all sidebar codes

## Slide 55: MEDECO RESEARCH: Results of Project
Covert and surreptitious entry in as little as 30 seconds: standard requires 10-15 minutes
Forced entry: four techniques, 30 seconds, affect millions of locks
Complete compromise of key control
  Duplication, replication, simulation of keys
  Creation of bump keys and code setting keys
  Creation of top level master keys

## Slide 56: RESULTS OF PROJECT: Bumping
Reliably bump open Biaxial and m3 locks
Produce bump keys on Medeco blanks and simulated blanks
Known sidebar code
Unknown sidebar code

## Slide 57: MEDECO BUMP KEY

## Slide 58: RESULTS OF PROJECT: Key Control and Key Security
Total compromise of key control and key security, vital to high security locks
  Duplicate, replicate, simulate keys for all m3 and some Biaxial keyways
    Restricted keyways, proprietary keyways
    Government and large facilities affected
  Attack master key systems
  Produce bump keys
  Produce code setting keys

## Slide 59: SIMULATED BLANKS: Any m3 and Many Biaxial Locks

## Slide 60: SIMULATED BLANKS

## Slide 61: M3 SLIDER: Bypass with a Paper clip

## Slide 62: SECURITY OF m3: High Tech Wire!

## Slide 63: RESULTS OF PROJECT: Picking
Pick the locks in as little as 30 seconds
Standard picks, not high tech tools
Use of another key in the system to set the sidebar code
Pick all pins or individual pins
Neutralize the sidebar as security layer

## Slide 64: PICKING A MEDECO LOCK

## Slide 65: RESULTS OF PROJECT: Decode Top Level Master Key
Determine the sidebar code in special system where multiple sidebar codes are employed to protect one or more locks
Decode the TMK
OWN the system

## Slide 66: RESULTS OF PROJECT: Forced Entry Techniques
Deadbolt attacks on all three versions
  Deadbolt 1 and 2: 30 seconds
  Deadbolt 3: New hybrid technique of reverse picking
Mortise and rim cylinders
  Prior intelligence + simulated key
Interchangeable core locks

## Slide 67: DEADBOLT ATTACK

## Slide 68: DEADBOLT BYPASS: 2$ Screwdriver + $.25 materials

## Slide 69: MORTISE CYLINDER

## Slide 70: MORTISE ATTACK

## Slide 71: CONNECTING THE DOTS
CRITICAL FAILURES
Original  Biaxial
  pin design
  code assignment
Biaxial - m3 design
  M3 slider geometry = .040” offset
  Key simulation
  .007” keyway widening

## Slide 72: MORE DOTS!
FORCED ENTRY
Original Deadbolt design
Fatal design flaw: 30 seconds bypass
Later deadbolt designs: new attacks
Mortise and rim cylinders
Inherent design problem: .065” plug

## Slide 73: MORE DOTS: BILEVEL LOCK
2007 Bilevel locks introduced
Integrate low and high security to compete
Flawed design, will affect system security when integrated into high security system
Borescope decoding of aft pins to compromise security of entire system

## Slide 74: CONNECTING THE DOTS: The Results
Biaxial Code assignment: Reverse Engineer for all non-master key systems
Gate tolerance: 4 keys to open
NEW CONCEPT: Code Setting keys
Sidebar leg-gate interface: NEW CONCEPT: Setting sidebar code
M3 Wider keyway: Simulated blanks
Slider design: paper clip offset

## Slide 75: 4 KEYS TO THE KINGDOM

## Slide 76: LESSONS TO BE LEARNED
Patents do not assure security
Apparent security v. actual security
40 years of invincibility means nothing
New methods of attack
Corporate arrogance and misrepresentation
“If it wasn’t invented here” mentality
All mechanical locks have vulnerabilities

## Slide 77: REAL WORLD ATTACK: Bumping a Medeco Lock

## Slide 78: OPEN IN THIRTY SECONDS
Setting the Sidebar Code
Conventional pick tools

## Slide 79: OPEN IN THIRTY SECONDS: Cracking one of the most secure locks in America
© 2008 Marc Weber Tobias and
Tobias Bluzmanis
www.securitylaboratories.org
mwtobias@securitylaboratories.org